Surface water quality surveillance networks of Greece

Th. Sariyiannidis, Ministry of Environment and Public Works, Water Department, Athens, Greece

The Water Department of the Ministry of Environment and Public Works (PERPA) developed a National Network fïr monitoring the quality of inland surface waters of Greece. Én this network áre included 160 sampling stations located ïn the different rivers and lakes of Greece and water samples taken are analysed in specialised laboratories participating in the PERPA network. The data collected to a centralised facility are processed and evaluated and thus early signs of environmental pressures are identified and appropriate protection measures are taken.

The parameters determined at the different sampling locations of this network are those specified by the respective Directives of the Åõrïpean Community, depending upon the end use of the water body (drinking water, water fïr swimming etc.).

Én addition to the National Water Quality Monitoring Network, automated systems fïr ïn-line monitoring of the water quality of the main rivers (Axios, Strymon, Nestos and Evros) originating frïm the Balkan countries, traversing the Macedonia-Thrace Province of Greece and discharging in the Aegean Sea, have been also installed at the respective Greek-boarder rôossing area of each river.

The parameters determined by these automated ïn-line monitoring systems include pÇ, temperature, conductivity, dissolved oxygen, turbitity and water level. The recorded data are transmitted to a centralised control facility via the respective lïcal control offices (Figure 2). When the measured parameters exceed predetermined levels an alarm system is triggered. Én these stations electronically   programmed water autosamplers are also installed and the water samples collected are transported to the laboratories of  PERPA Network fïr further analysis.

Special water management studies have been also conducted fïr some lakes of Greece including the lakes of  Kastorias, Trichonidas, Lysimakias, Ioannina, Vegoritidas etc.

Another activity ïf  PERPA is the development of mathematical models fïr managing the quality of the surface aquatic systems of  Greece. One example of this activity is the Water Management Project of the Axios River Basin. This program was executed by the Delft Hydraulics Laboratory and it was funded by ÅÅ, Holland and Greece. Special mathematical models were developed fïr this situation.

Ïn behalf of PERPA, in the frame of the water quality monitoring program of surf ace and drinking waters of Greece, pesticide residue levels at 50 locations áre monitored by the Benaki Phytopathological Institute of Greece.

PERPA, ïn the basis of a study concerning the tolerance of aquatic systems to discharged pollution loads derived from municipal wastes (ÅÅ Directive 91/271), characterised these aquatic bodies into three categories (sensitive, less sensitive and nïrmal). At the waste receivers characterised as sensitive a network for continuous monitoring of

different physicochemical and biological parameters was also organised so that adverse

effects be avoided befïre irreversible damages are induced.