Off-line SPE and GC-MSD ion trap fοr monitoring pesticides in aquatic systems

Ε. Papαdopouiou-Mourkidou and J. Patsias

# Aristotle University, Pesticide Science Laboratory, Thessaloniki, Greece

### ABSTRACT

Α rapid method for the analysis at trace levels of 96 target analytes

in aquatic systems has been developed. The analyte list includes pesticide parent compounds from a variety of chemical and biological classes αηd some of their ma jor metabolites and degradation products. Analytes were extracted from 1L filtered water samples by of f-line solid phase extraction (SPE) οn three tandem Cl8 Sep-Pak cartridges. The sorbed analytes eluted with ethyl acetate weτe determined by gas chromatography-ion trap mass spectrometry (GC-ITMS), the mass spectrometer operated in the electron impact (ΕΙ) ionization mode. The mean recoveries at the 0.5 ppb fortification level for the two thirds of the analytes ranged from 75 tο 120% the recoveries of less than one third of the analytes ranged from 50 to 75% and the recoveries of the 10 relatively most polar analytes ranged from 12 to 509.

The limit of detection (LOD) for 69 analytes was 0.01 ppb οr better; the LOD f οr 18 analytes was 0.05 ppb or better; for captan, carbofenothion, decamethrin, demeton-S-methyl sulphone, fensulfothio,, deisopropylatrazine and metamitron the LOD was 0.1 ppb and for chloridazon and tetradifon 0.5 ppb. The analyte identification process following each chromatographic run was completed in less than two min. Identifications were made at S/Ν>3. Quantificatification of the majority of the analytes was made at the base mass. The system was evaluated for monitoring pesticides in surf ace and ground water samples of Macedonia, Greece:

#### INTRODUCTION

The occurrence of pesticides and their conversion products in aquatic

Systems is of major concern world-wide. Pesticide monitoring studies ίn the Axios River basin  indicated that with respect to surface and ground water quality about 120 pesticides including also some of their major concersion products are of main environmental concern in this area (1&2). Ιn these studies analyses were made using GC in association with selective detection systems (NPD, FPD, ECD and MSD) and HPLC-DAD (3). Α rapid system f or the reliable identification and determination at trace levels of most of the GC-amenable compounds of interest is described here.

## EXPERIMENTAL SECTION

Α Τracker/Μagnum iοn trap mass spectrometer (ITMS) (Finnigan ΜΑΤ) associated with a Varian (Varian Instruments) , Model 3300, gas chromatograph was used. The system was controlled by the Magnum (Finnigan ΜΑΤ) data system operated οn an ΙΒΜ compatible computer. Details about the operating conditions of the GC-ITMS system, sample preparation and analyte identification and quantification procedures are given in Reference (4).

## RESULTS AND DISCUSSION

Α wide chemical range of 96 compounds (triazines, chloracetanilides, phenylureas, dinitro-anilines, organophosphorus, pyrethroids, organochlorines and miscellaneous other chemical classes) including also some of their major metabolites and degradation products comprised the target analyte list of this project. The list of the analytes of interest is presented in Table 1.

The mean recoveries at the 0.5 ppb level for the majority of the analytes (60 compounds) extracted by SPE ranged from 75 to 120%. The respective recoveries of 26 analytes ranged from 50 to 75%. The latter group contains the most lipophilic compounds among the target analytes such as the organochlorines and the pyrethroids. For these compound despite of their high (1000 ml) breakthrough volumes, relatively low recovery values were also recorded when water samples were analysed by οn-line SPE-HPLC-DAD system utilising PRP-1 cartridges (5).

The mean recoveries of the relatively polar analytes (chloridazon, fenpropimorph, deethylatrazine (G-30), isofenphos, metamitron, molinate and monocrotophos) ranged from 30 to 50%, while the respective recoveries of the most polar analytes including demeton-S-methyl sulphone, dimethoate and deisopropylatrazine were 18.4, 24.1 and 12.2%, respectively. The low recoveries of the polar analytes were obviously due to the fact that the sample volume exceeded by far their respective breakthrough volumes (5).

The precision of the SPE system, expressed by the Relative Standard Deviation (R.S.D.) of the mean recoveries values derived from the analysis of triplicate samples fortified at 0.5 ppb, f or the majority of the analytes was better than 109 (Table 1). The R.S.D. values of chloridazon, decamethrin, demeton-S-methyl sulphone, fenpropimorph, metamitron and molinate ranged from 14 to 18%. These analytes, except for decamethrin, are among the most polar compounds included in the target analyte list, their recoveries being 50%, and the feasibility of GC analysis marginal.

Ιn order to evaluate the SPE system, the recoveries of analytes when 1 L fortified samples at 0.5 ppb extracted by liquid-liquid partition (LLP) with dichloromethane were also determined. The profile of the % mean recovery values was approximately the same by both extraction methods while the extraction precision, expressed by the respective R.S.D. values, was slightly better with SPE than LLP (Table 1). The mean recoveries of the polar analytes, except for monocrotophos, as expected, were higher when samples were extracted by LLP while the recovery of molinate was approximately the same by both LLP and SPE (Table 1). Apparently, the most significant parameter in reduced recovery values of the thiocarbamate herbicide, molinate, is its relatively high vapour pressure and as a result a substantial amount is lost during concentration of either the dichloromethane or ethyl acetate extract. Therefore,

for the extraction of the target analytes from water samples a SPE technique was selected as being as efficient, more precise, more environmentally friendly, less dangerous to the analyst and much faster than the conventional lίquid-liquid partition (LLP) method. However, water extracts derived by LLP were significantly cleaner than the respective extracts derived by SPE.

The LOD fοr more than the two thirds ( 65 compounds) of the analytes of interest was better than 0.01 while among these compounds 53 analytes could be detected at less than 5 ρρt level. For 19 analytes (chlorpyrifos-ethyl, chlorothalonil, desmetryn, dimethoate, endosulfan Ι &ΙΙ,

endosulfan sulfate, endrin. ethion, fenvalerate ΙΙ, flutriafol, heptachlor epoxide, 1inuron, monocrotophos, paraoxon. paraoxon-methyl, pyrazophos, quinalphos and triazophos) the LOD was set at 0.05 ppb. For captan, carbofenothion, decamethrin, demeton-S-methyl sulphone, fensulfothion, deisopropylatrazine (G-28) and metamitron the LOD was set at 0.1 ppb while for chloridazon and tetradifon the 0.5 ppb level.

The LOD values reported in Table 1 are comparable and in some cases they are even better than those reported by Mattern et al (1991) for 20 pesticides extracted from surf ace waters by SPE on XAD-2/XAD-7 resins and analysed by CG/ITMS operated in the chemical ionisation mode (CI). However, Mattern et a1. (1991) defined LODs at S/Ν>5 whereas ίn this work the finger print information of the ΕΙ spectra allowed reliable identifications based on  full mass spectra scans at S/Ν>3. The lower sensitivity attained at the ΕΙ mode due to more fragmentation of the analytes is compensated by the increased confirmatory structural information of the ΕΙ mass spectrum.

The system operated in the auto-search/auto-integration mode was evaluated with the analysis of field surf ace and ground waters collected from the Axios River basin. Ιn Figure 1 are shown sample data from the analysis of a samples collected from the Axios River at the Greek/FYROM boarder in June, 1994. Molinate, a-BHC and b-BHC were found at 0.017, 0.070 and 0.010 ppb level, respectively. Ιn Figure 2 are shown data from the analysis of a soil water sample taken from 160 cm depth of a corn field located in the same area. Ιn this sample, deethylatrazine (G-30), atrazine, carbofuran and lindane at 0.216, 0.230, 0.146 and 0.535 ppb level, respectively, were determined.

##### CONCLUSIONS

Α GC-ΙΤΜS system operated in the ΕΙ mode and associated with off-line

SPE of field water samples can be used routinely in pesticide analysis at the low ρρt level.

The inherent increased sensitivity of the ion trap MS a1lοws the use of the analyte full scan

mass spectra reliable identification even at the low levels detection and/or determination.

###### ACKNOWLEDGEMENTS

This work was supported by a grant from European Community, Proj.

Νο. EVSV-CT92-0105 and the Greek Ministry of Agriculture via the Interreg Program.

## REFERENCES

## 1. Ε. Papadopoulou-Mourkidou. Eighth IUPAC International Congress of Pesticide      Chemistry, Vol. 2, ρ. 825, Washington DC, 1994.

2. Ε. Papadopoulou-Mourkidou. Proceedings of Environmental Contamination, 6th International Conference, p. 453, Delphi, Greece, 1994.

3. Ε. Papadopoulou-Mourkidou and J. Patsias. J. Chromatogr. Accepted for publicatiοn (1995).

4. J. Patsias and Ε. Papadopoulou-Mourkidou. d. Chromatogr. Submitted for publication (1995).

Table 1. Retention times (min), quantification masses, % mean recoveries and respective R.S.D. values and LODs of the target analytes.

Pesticide Reten. Quant. % Mean & Mean LOD

Time Mass Recoverya Recoverya ppb

(min) (m/z) (R.S.D.) (R.S.D.)

LLP SPE

alachlor 23.19 160 92 (10) 94 (3) 0.005

aldrin 25.26 66 37 (4) 59 (5) 0.01

ametryne 23.45 227 78 (13) 65 (8) 0.01

atrazine 20.26 200 97 (1) 93 (9) 0.005

azinphos-ethyl 37.45 132 (90%) 99 (1) 78 (4) 0.01

azinphos-methyl 36:11 132 (70%) 109 (2) 94 (2) 0.01

α-BHC 19.26 181 69 (12) 67 (8) 0.005

b-BHC 20.18 183 84 (9) 86 (3) 0.005

γ-BHC 20.40 181 74 (8) 82 (7) 0.005

d-BHC 21.44 181 90 (9) 89 (2) 0.01

cadusafos 19.08 159 85 (8) 82 (4) 0.01

captan 27.33 79 105 (16) 87 (3) 0.1

carbofenothion 32.25 157 75 (14) 51 (6) 0:1

carbοfuran 20.11 164 106 (1) 112 (5) 0.005

chlorfenvinphos 27.18 267 79 (8) 92 (2) 0.005

chioridazon 32.48 77 40 (32) 34 (18) 0.5

chlorobenzilate 31.03 139 (95%) 108 (3) 94 (3) 0:005

chloropropylate 31.02 251 87 (9) 90 (2) 0.005

chlorothalonil 21.14 Ζ66 95 (6) 90 (3) 0.05

chlorpyrifos-ethyl 25.19 197 (70%) 87 (9) 75 (5) 0.05

chlorpyrifos-methyl 23:02 286 84 (4) 79 (4) 0.005

chlorthiophos 31.28 269 74 (11) 54 (10) 0.01

coumaphos 39.36 362 106 (5) 86 (9) 0.01

cyanofos 20.52 109 77 (7) 80 (7) 0.005

o,p-DDE 28.21 246 66 (4) 59 (6) 0.005

pp,-DDE 29.43 246 71 (4) 57 (8) 0.005

DDD 31.2 235 83 (11) 72 (1) 0.01

DDT 32.45 235 103 (5) 72 (5) 0.005

decamethrin 52.0 181 92 (8) 52 (18) 0.1

demeton-S-methyl 24.14 169 102 (21) 18 (15) 0.1 sulfone

desmetryn 22.43 213 95 (11) 76 (10) 0.05

dialifos 37.55 208 89 (12) 88 (3) 0.01

diazinon 21.06 179 85 (8) 86 (3) 0.005

dicofοl 26.01 139 105 (5) 55 (9) 0.01

dieldrin 29.50 79 95 (10) 89 (1) 0.01

dimethoate 20.00 125 (50%) 88 (4) 24 (7) 0.05

endosulfan Ι 28.45 195 (90%) 76 (12) 99 (2) 0.05

endosulfan ΙΙ 31.06 195 97 (5) 92 (3) 0.05

endosulfan sulfate 32.38 272 112 (6) 89 (5) 0.05

endrin 30.42 81 84 (9) 94 (1) 0.05

ethion 31.25 231 89 (1) 76 (6) 0.05

ethofumesate 24.43 207 93 (1) 85 (5) 0.005

fenitrothion 24.29 125 96 (10) 88 (5) 0.01

fenpropimorph 25.41 128 67 (22) 21 (12) 0.01

fensulfothion 31.08 293 82 (8) 74 (7) 0.1

fenvalerate Ι 47.00 125 100 (7) 55 (10) 0.01

fenvalerate ΙΙ 48.16 125 98 (1) 56 (10) 0.05

fluometuron 18.00 72 84 (10) 84 (3) 0.005

flutriafοl 29.04 123 109 (1) 75 (4) 0.05

formothion 22.21 93 80 (11) 62 (1) 0.01

G-28 18.25 173 21 (9j 12 (4) 0.1

G-30 18.38 172 65 (4) 31 (6j 0.01

heptachlor 23.41 100 43 (9) 66 (3) 0.01

heptachlor epoxide 27.10 81 (85%) 78 (11) 85 (2) 0.05

isofenphos 27.10 58 77 (13) 44 (10) 0.01

linuron 24.49 61 94 (11) 95 (5) 0.05

malathion 24.58 125 (95%) 113 (5) 99 (2) 0.01

malaoxon 23.15 127 111 (8j 120 (5) 0.01

metamitron 30.14 104 59 (3) 20 (14) 0.1

metalaxyl 23.42 206 102 (7) 98 (2) 0.005

methacrifos 15.19 125 62 (4) 59 (6) 0.01

methidathion 28.10 145 100 (2) 85 (3) 0.005

methoxychlor 34.54 227 126 (4) 82 (7) 0.01

metolachlor 25.15 162 94 (2) 80 (8) 0.005

metobromuτon 22.26 61 98 (9) 88 (2) 0.01

mevinphos 13.41- 127 68 (5) 71 (2) 0.0005 (cis/trans) 13:46

molinate 16.18 126 (95%) 48 (12) 48 (18) 0.005

monocrotophos 19.07 127 11 (13) 32 (8) 0.05

monolinuron 20.22 61 86 (10) 78 (3) 0.005

parathion 25.37 109 94 (9) 91 (6) 0.01

parathion-methyl 23.15 109 89 (10j 97 (3) 0.003

paraoxon 23:59 109 82 (9) 93 (4) 0.05

paraoxon-methyl 21.32 109 76 (14) 89 (6j 0.05

pendimethalin 26.49 252 97 (4) 72 (2) 0.005

cis-permethrin 39.17 183 100 (3) 53 (9) 0.005

trans-permethrin 39.37 183 105 (7) 67 (4) 0.005

phenthoate 27:31 274 86 (10) 78 4) 0.01

phosalone 36.00 182 89 (10) 93 (3) 0.01

phosmet 34.29 160 95 (5) 99 (5) 0.005

pirimifos-ethyl 26.21 168 (80%) 83 (6) 73 (5) 0.005

pirimifos-methyl 24.26 276 (90%) 74 (11) 78 (5) 0.01

procymidone 27.39 96 84 (11) 86 (7) 0.005

prometryne 23.59 184 100 (4) 73 (6) 0.001

ρrοpach1οr 17.35 120 80 (1) 73 (4) 0.005

propanil 22.50 161 101 (5) 83 (8) 0.01

prothoate 23.02 115 78 (10) 76 (4) 0:01

pyrazophos 37.22 221 88 (8) 88 (1) 0:05

quinalphos 27.35 146 89 (4j 79 (2) 0.05

simazine 20.14 201 72 (11) 87 (1) 0.005

terbumeton 20.36 210 79 (17) 77 (8) 0.01

terbuthylazine 20.56 214 93 (4) 75 (8) 0.005

terbutryne 24.33 226 83 (5) 71 (9) 0.01

tetrachlorvinphos 28.25 109 (90%) 93 (7) 114 (3) 0.005

tetradifon 35.43 75 91 (2) 82 (1) 0.5

triazophos 31.59 161 89 (7) 93 (4) 0.05

trifluraline 18.44 306 52 (16) 69 (2) 0.005

α/. Mean recoveries weτe determined at 0.5 ppb fοrtification level.