PRINCIPLES OF WASTEWATER ENGINEERING

G. P. SAKELLAROPOULOS, P. SAMARAS

DEPARTMENT OF CHEMICAL ENGINEERING, AUTH

CHEMICAL PROCESS ENGINEERING RESEARCH INSTITUTE

- WASTEWATER CHARACTERISTICS-QUALITY

- WASTEWATER TREATMENT

- PRIMARY		PHYSICAL

- SECONDARY	BIOLOGICAL

- ADVANCED		CHEMICAL/PHYSICAL/BIOLOGICAL

- SLUDGE TREATMENT

- DISPOSAL

- SLUDGE / WASTEWATER

- RECLAMATION AND REUSE

ASSOCIATED PROBLEMS IN WASTEWATER ENGINEERING

WASTEWATER QUALITY

FLOW-RATE VARIATION

BEST TREATMENT PROCESSES

DESIGN CRITERIA

- DESIGN PERIOD

- POPULATION DATA

- WASTEWATER PRODUCTION

- REGULATIONS

- TREATMENT PROCESS SELECTION

- TECHNICAL-ECONOMIC STUDY

- ENVIRONMENTAL IMPACT ASSESSMENT

WASTEWATER CHARACTERISTICS

PHYSICAL

CHEMICAL

BIOLOGICAL

EXPRESSING ANALYTICAL RESULTS

mg/l		ppm=mg/106mg

PHYSICAL PARAMETERS

TOTAL SOLIDS

TEMPERATURE

COLOR

ODORS

TOTAL SOLIDS

Residue after evaporation at 103-105°C

SETTLEABLE-NON SETTLEABLE

SUSPENDED -FILTERABLE (1,2 μm)

COLLOIDAL (1 nm-1 μm)-DISSOLVED (<1 nm)

VOLATILE-FIXED (550°C)

CHEMICAL CHARACTERISTICS

- ORGANIC MATTER

- PROTEINS (40-60%)

- FATS-OILS (10%)

- CARBOHYDRATES (25-50%)

- SYNTHETIC COMPOUNDS

- INORGANIC MATTER

- GASES

ORGANIC CONTENT MEASUREMENT

BIOCHEMICAL OXYGEN DEMAND (BOD5)

CHEMICAL OXYGEN DEMAND (COD)

TOTAL ORGANIC CARBON (TOC)

THEORETICAL OXYGEN DEMAND (ThOD)

TYPICAL DOMESTIC WASTES

BOD5/COD  0.4 - 0.8

BOD5/TOC  1.0 - 1.6

LIMITATIONS OF BOD TEST

MEASUREMENT OF BIODEGRADABLE ORGANICS

INFLUENCE OF TOXIC WASTES

NEED FOR SEEDING

LONG TEST

INORGANIC MATTER

pH

CHLORIDES

ALKALINITY

NITROGEN

PHOSPHORUS

SULFUR

HEAVY METALS

GASES

DISSOLVED OXYGEN

HYDROGEN SULFIDE

METHANE

BIOLOGICAL CHARACTERISTICS

........IN ADDITION: BIOASSAYS

....AND WHY BIOASSAYS?

CHEMICAL-PHYSICAL TESTS NOT SUFFICIENT ENOUGH

INTERACTIONS BETWEEN CHEMICALS

A LARGE NUMBER OF CHEMICALS

LIVING ORGANISMS WITH DIFFERENT SENSITIVITY

BIOASSAYS GOALS

- PROTECTION OF A WASTEWATER TREATMENT PLANT

INFLUENTS/CO-TREATMENT

- EVALUATION OF EFFECTIVENESS

INFLUENTS-EFFLUENTS

- PROTECTION OF AN ECOSYSTEM

EFFLUENTS

Typical composition of untreated domestic wastewater

|  |  | Concentration |
| --- | --- | --- |
| Contaminant | Unit | Weak | Medium | Strong |
| Solids, total (TS) | mg/L | 350 | 720 | 1200 |
| Dissolved, total (TDS) | mg/L | 250 | 500 | 850 |
| Fixed | mg/L | 145 | 300 | 525 |
| Volatile | mg/L | 105 | 200 | 325 |
| Suspended solids (SS) | mg/L | 100 | 220 | 350 |
| Fixed | mg/L | 20 | 55 | 75 |
| Volatile | mg/L | 80 | 165 | 275 |
| Settleable solids | mL/L | 5 | 10 | 20 |
| BOD5 | mg/L | 110 | 220 | 400 |
| Total organic carbon (TOC) | mg/L | 80 | 160 | 290 |
| Chemical oxygen demand (COD) | mg/L | 250 | 500 | 1000 |
| Nitrogen (total as N) | mg/L | 20 | 40 | 85 |
| Organic | mg/L | 8 | 15 | 35 |
| Free ammonia | mg/L | 12 | 25 | 50 |
| Nitrites | mg/L | 0 | 0 | 0 |
| Nitrates | mg/L | 0 | 0 | 0 |
| Phosphorus (total as P) | mg/L | 4 | 8 | 15 |
| Organic | mg/L | 1 | 3 | 5 |
| Inorganic | mg/L | 3 | 5 | 10 |
| Chlorides | mg/L | 30 | 50 | 100 |
| Sulfate | mg/L | 20 | 30 | 50 |
| Alkalinity (as CaCO3) | mg/L | 50 | 100 | 200 |
| Grease | mg/L | 50 | 100 | 150 |
| Total coliform | no/100 mL | 106-107 | 107-108 | 107-109 |

WASTEWATER TREATMENT

PRELIMINARY/ PRIMARY TREATMENT

- SCREENING

- FLOW EQUILIBRATION

- GRIT REMOVAL

- FLOTATION

- SEDIMENTATION

SECONDARY TREATMENT

BIOLOGICAL TREATMENT-SEDIMENTATION

- SUSPENDED SOLID SYSTEMS

ACTIVATED SLUDGE

LAGOONS

- FIXED SOLID SYSTEMS

BIOLOGICAL FILTERS-TOWERS-DISCS

ADVANCED TREATMENT

ACTIVATED CARBON ADSORPTION

FLOCCULATION-COAGULATION

AMMONIA REMOVAL

PHOSPHORUS REMOVAL

REVERSE OSMOSIS

ION EXCHANGE

DISINFECTION

PROCESS SELECTION

IMPORTANT FACTORS

SELECTION BASED ON KINETICS

REACTOR TYPES

REACTOR COMBINATIONS

MASS BALANCE

PERFORMANCE COMPARISON

IMPACT OF FLOW VARIATION

SCREENING

- PARALLEL BARS-RODS

- WIRE CLOTH

HAND -MECHANICALLY CLEANED

SEDIMENTATION

DISCRETE PARTICLE SETTLING

Selection of particle (d)

Estimation of Vc

Q=A*Vc

Vc=overflow rate m3/m2/day

FLOTATION

INTRODUCTION OF FINE BUBBLES

- AIR INJECTION -LIQUID UNDER PRESSURE (DAF)

- AERATION AT ATMOSPHERIC PRESSURE

- VACUUM APPLICATION

FILTRATION

TYPES OF FILTERS

PARTICLE REMOVAL MECHANISMS

CHEMICAL PRECIPITATION

CHEMICALS USED

ALUM Al2(SO4)3

FERRIC CHLORIDE FeCl3

LIME Ca(OH)2

ACTIVATED CARBON ADSORPTION

PRODUCTION OF ACTIVATED CARBON

GRANULAR-POWDER

REGENERATION

DISINFECTION

# CHEMICAL AGENTS

CHLORINE

OZONE

HYDROGEN PEROXIDE

## PHYSICAL AGENTS

HEAT

LIGHT

## MECHANICAL MEANS

BIOLOGICAL PROCESSES

OC(CHONS)+M/O+O2---CO2+NH3+M/O

M/O+O2----CO2+H2O+NH3+ENERGY

### IMPORTANT PARAMETERS

RETENTION TIME (HYDRAULIC-MCRT)

#### MLSS

F/M (kg FOOD/DAY/kg M/O)

ACTIVATED SLUDGE PROCESS

DESIGN FEATURES

REACTOR TYPE

LOADING CRITERIA

SLUDGE PRODUCTION

OXYGEN REQUIREMENTS

NUTRIENT REQUIREMENTS

SLUDGE TREATMENT

PRELIMINARY OPERATIONS

(DEGRITTING-BLENDING)

# THICKENING

STABILIZATION

DIGESTION (ANAEROBIC-AEROBIC)

COMPOSTING

# CONDITIONING

DISINFECTION

DEWATERING

HEAT DRYING

LAND APPLICATION

##### NATURAL TREATMENT SYSTEMS

###### Slow rate

Rapid infiltration

Overland flow

Wetland application

Floating aquatic plants

Comparison of expected effluent quality of treated water from slow-rate, rapid infiltration, and overland-flow natural treatment systems

|  | Value, mg/L |
| --- | --- |
|  | Slow-rate | Rapid infiltration | Overland-flow |
| Constituent | Average | Maximum | Average | Maximum | Average | Maximum |
| BOD | <2 | <5 | 2 | <5 | 10 | <15 |
| Susp. Solids | <1 | <5 | 2 | <5 | 15 | <25 |
| Ammonia-N | <0,5 | <2 | 0,5 | <2 | 1 | <3 |
| Total N | 3 | <8 | 10 | <20 | 5 | <8 |
| Total P | <0,1 | <0,3 | 1 | <5 | 4 | <6 |

Comparison of design features of alternative natural treatment systems

| Feature | Slow-rate Type 1 | Slow-rate Type 2 | Rapid infiltration | Overland-flow | Wetland application | Floating aquatic plant |
| --- | --- | --- | --- | --- | --- | --- |
| Application techniques | Sprinkler or surface | Sprinkler or surface | Usually surface | Sprinkler or surface | Sprinkler or surface | Surface |
| Annual hydraulic loading, ft/y | 5,6-20 | 2,0-6,7 | 20-300 | 24-186 | 18-60 | 18-60 |
| Area required, ac/(Mgal/d) | 56-200 | 170-550 | 3,7-56 | 6-45 | 18-62 | 18-62 |
| Minimum preapplication treatment provided | Primary sedimentation | Primary sedimentation | Primary sedimentation | Screening | Primary sedimentation | Primary sedimentation |
| Disposition of applied wastewater | Evapotranspiration and percolation | Evapotranspiration and percolation | Mainly percolation | Surface runoff and evaporation with some percolation | Evapotranspiration percolation and runoff | Some evapotranspiration |
| Need for vegetation | Required | Required | Optional | Required | Required | Required |

Comparison of site characteristics for natural treatment systems

| Characteristics | Slow-rate | Rapid infiltration | Overland-flow | Wetland application | Floating aquatic plants |
| --- | --- | --- | --- | --- | --- |
| Climatic conditions | Storage often needed for cold weather and during precipitation | None (possibly modify operation in cold weather) | Storage often needed for cold weather and during precipitation | Storage may be needed for cold weather | Storage may be needed for cold weather |
| Depth to groundwater | 2-3 ft (minimum) | 10 ft (lesser depths acceptable where underdrainage is provided) | Not critical | Not critical | Not critical |
| Slope | Less than 15% on cultivated land; less than 40% on forester land | Not critical; excessive slopes require much earthwork | Finish slopes 1-8% | Usually less than 5% | Usually less than 5% |
| Soil permeability | Moderately slow to moderately rapid | Rapid (sands, loamy sands) | Slow (clay, silts and soils with impermeable barriers) | Slow to moderate | Slow to moderate |

Principal steps in the design of natural systems

| Slow-rate | Rapid infiltration | Overland-flow | Constructed wetlands and floating aquatic plants |
| --- | --- | --- | --- |
| Site evaluation and selection | Site evaluation and selection | Site evaluation and selection | Site evaluation and selection |
| Determination of pretreatment level | Determination of pretreatment level | Determination of pretreatment level | Determination of pretreatment level |
| Crop selection | Selection of distribution method | Selection of distribution method | Vegetation selection and management |
| Distribution system selection | Determination of design hydraulic-loading rates | Determination of system design parameters | Determination of design parameters |
| Determination of loading rates | Determination of design operating cycles | Determination of storage requirements | Vector control measures |
| Determination of land area requirements | Determination of land requirements | Calculation of land area requirements | Detailed design of system components |
| Determination of storage volume requirements | Layout of infiltration area | Layout of system components | Determination of monitoring requirements |
| Determination of monitoring requirements | Layout and sizing of effluent recovery system | Selection of cover crop |  |
|  | Determination of storage requirements | Detailed design of system components |  |
|  | Determination of monitoring requirements | Determination of monitoring requirements |  |

##### WASTEWATER RECLAMATION-REUSE

| Wastewater reuse categories | Potential constraints |
| --- | --- |
| Agricultural irrigation |  |
| Crop irrigation |  |
| Commercial nurseries |  |
| Landscape irrigation | Surface and groundwater pollution if not properly managed |
| Park | Marketability of crops and public acceptance |
| School yard | Effect of water quality, particularly salts, on soil and crops |
| Freeway median | Public health concerns related to pathogens (bacteria, viruses, parasites) |
| Golf course | Use area control including buffer zone. May result in high user costs |
| Cemetery |  |
| Greenbelt |  |
| Residential |  |
| Industrial recycling and reuse |  |
| Cooling | Constituents in reclaimed water related to scaling, corrosion, biological |
| Boiler feed | growth and fouling |
| Process water | Public health concerns, particularly aerosol transmission of |
| Heavy construction | pathogens in cooling water |
| Groundwater recharge |  |
| Groundwater replenishment | Organic chemicals in reclaimed wastewater and their |
| Salt water intrusion control | toxicological effects. Total dissolved solids, nitrates, and |
| Subsidence control | pathogens in reclaimed wastewater |
| Recreational/environmental uses |  |
| Lakes and ponds | Health concerns of bacteria and viruses |
| Marsh enhancement | Eutrophication due to N and P in receiving water |
| Streamflow augmentation | Toxicity to aquatic life |
| Fisheries |  |
| Snowmaking |  |
| Nonpotable urban uses |  |
| Fire protection | Public health concerns on pathogen transmitted aerosols |
| Air conditioninng | Effects of water quality on scaling, corrosion, biological growth, fouling |
| Toilet flushing | Cross-connection |
| Potable use |  |
| Blending in water supply | Constituents in reclaimed wastewater, especially trace organic |
| Reservoir | chemicals and their toxicological effects |
| Pipe to pipe water supply | Aesthetic and public acceptance |
|  | Health concerns about pathogen transmission, particularly viruses |